FEATURES OF SMITH & WESSON LARGE FRAME MODEL 629

BASIC FEATURES Caliber: .44 magnum /.44 special The Smith & Wesson Large Frame Model 629 uses two types of ammunition: .44 magnum and .44 special. Magnum has the most gunpowder and a larger casing. As a result, magnum bullets have a higher muzzle velocity and energy when fired. Special ammunition is slightly smaller than magnum bullets and uses less gunpowder. It has a lower muzzle velocity and energy. Capacity: 6 rounds This gun can hold up to six rounds (bullets) at a time. Barrel Length: 6 inches Overall Length: 11 5/8 inches Weight Empty: 45 oz. Material: Stainless Steel BASIC TERMINOLOGY Barrel: The barrel is the metal tube through which the bullet is fired. The length of a barrel is measured from the muzzle to the cylinder (but does not include the cylinder). Caliber: The size of the bullet used in a particular handgun. This is determined by the diameter of the bullet, measured either in millimeters or in hundredths of an inch. Cylinder: The rotating drum, found on revolvers, which contains multiple chambers where the ammunition is stored. A cylinder often has six chambers, but some are made with as many as ten. When a revolver is discharged, the cylinder can be manually rotated to bring the next chamber in line with the barrel. Frame: The basic structure or housing to which the other components are attached. Grip: The point at which the user holds the handgun during use. Grips are usually made of wood, rubber, or synthetic materials, and can be custom-designed to fit the user's hand. The grip is generally an integral part of the frame. Hammer: A metal rod or plate that strikes the cartridge primer to detonate the powder. Sights: The device(s) on top of a barrel that allow the gun to be aimed. Trigger Guard: A loop of metal that extends down from the frame and encircles the trigger. It is designed to prevent the trigger from snagging as the handgun is removed from or placed into a holster.